## Slide 1: Every AI command is checked before the robot moves
DGS Cyber Twin PEP in the UnifoLM-WMA packing loop · MuJoCo simulation, no physical robot
AI model
UnifoLM-WMA-0 / replay
16 actions per request
Postino
robot_client.py
asks the PEP before acting
PEP · Cyber Twin
validates · logs
operator override
Robot
MuJoCo simulator
moves only on ALLOW
actions
check
if ALLOW
Three checks in every cycle
1
Before the start pose
Holds until a person clicks Arma robot (disarmed → DENY G1D-107)
2
Before each 16-step chunk
Arm joints only, within URDF limits, ≤ 3.0 rad/s. Otherwise DENY: drop it, ask the model again
3
Before every step
Still armed? E-stop or disarm aborts the chunk mid-motion
What the PEP stops
G1D-101 DENY
Revoked or unknown identity
G1D-102 DENY
Values past the limits
G1D-103 DENY
Wrong robot (out of scope)
G1D-104 DENY
Privilege escalation
G1D-105 DENY
Replayed request
G1D-106 DENY
Spoofed identity
G1D-107 DENY
Move while disarmed
G1D-108 DENY
Request not via the PEP
G1D-200 ALLOW
Valid chunk: ALLOW
Fail-closed: no PEP answer, no motion · Identity set by the postino, not the model · Every decision logged · Not covered: direct DDS access (isolate that network)
Notes: The model's output is treated as untrusted. The postino (robot_client.py) asks the Cyber Twin's PEP before the start pose, before each 16-step chunk, and before every single step. A chunk runs only on ALLOW: arm joints only, within the URDF limits, no faster than 3.0 rad/s. Identity, route and target are set by the postino, never taken from the model. If the twin does not answer, nothing moves. Every decision is logged. The operator can arm, disarm, E-stop, revoke the identity, or switch to monitor mode. Limit: the PEP guards the postino's path only, so on a real robot the DDS network must be isolated.